## Slide 1
WIEG & WCMA Legislative Conference
March 7, 2018
Wisconsin DNR Program Updates
Bart Sponseller
Deputy Division Administrator
Environmental Management Division
Wisconsin Department of Natural Resources
Wisconsin
Department of Natural Resources

## Slide 2: Air Program Topics
EPA items on the horizon (ozone implementation, “once in always in” policy, NSR reform, monitoring citizen science)
1-hour NO2 NAAQS Implementation
Addressing PM2.5 in Permits
Collaborative permit process
Wisconsin
Department of Natural Resources

## Slide 3
Wisconsin
Department of Natural Resources
2015 Ozone NAAQS Designations
In September 2016, Gov. Walker recommended that all counties in Wisconsin be designated as attainment of the 2015 ozone NAAQS (70 ppb).
In April 2017, DNR submitted additional information supported the recommendation including data showing the impact of transport on state ozone levels and the maximum extent of 70 ppb design values in the state.
On November 6, EPA designated all but 16 counties in Wisconsin as attainment/unclassifiable for the 2015 ozone NAAQS; EPA deferred action on the 16 counties.

## Slide 4
Wisconsin
Department of Natural Resources
2015 Ozone NAAQS Designations
On December 20, 2017 EPA took action on the remaining counties, proposing to designate them all as attainment/unclassifiable except for:
  Kenosha County (partial)
  Washington, Waukesha, Ozaukee, Milwaukee, and Racine counties
  Sheboygan County (partial), Manitowoc County (partial), Door County (partial)
On Feb. 28, state submitted additional technical information for EPA to consider. EPA also received many comments from state organizations asking that any nonattainment areas be smaller than those proposed by EPA.
Between April 19-30, 2018, EPA is expected to finalize designations.
Nonattainment new source review permitting requirements (including LAER, offsets…) will apply in any nonattainment areas, once finalized.

## Slide 5
Wisconsin
Department of Natural Resources
EPA’s Intended 2015 Ozone NAAQS Nonattainment Area Designations
All areas of Wisconsin
Data from EPA’s 120-day letter of 12/20/17 and
DNR submittal to EPA of 4/20/17

## Slide 6: Ozone standards implementation
EPA is currently implementing two ozone standards
  2008 ozone NAAQS (75 ppb)
  2015 ozone NAAQS (70 ppb)
State has continued responsibilities re: two 2008 ozone NAAQS nonattainment areas
  Sheboygan County and partial Kenosha County
DNR continues to work with EPA to develop strategies to ensure these areas attain the 2008 ozone standard
Wisconsin
Department of Natural Resources

## Slide 7: Ozone transport
Studies and analyses continue to show the elevated ozone levels measured along the Wisconsin lakeshore are due to out of state emissions
Example (right) of wind pollution rose analysis and source apportionment modeling results for Sheboygan Kohler-Andrae monitoring site
Wisconsin
Department of Natural Resources

## Slide 8: Once In Always In Policy
Once in always in policy affects facilities subject to maximum achievable control technology (MACT) standards
  Old policy from May 1995 “Seitz Memo”
A major source of hazardous air pollutants (HAPs) is permanently subject to the MACT standard at the “first compliance date” of the standard even if the source is later able to limit its HAP emissions below the major source thresholds
Wisconsin
Department of Natural Resources

## Slide 9
New Policy - January 25, 2018
  A major source may take enforceable limits on its HAP emissions below the applicable major source thresholds for HAPS
  Once limits are taken, the source is no longer subject to the MACT standard
  EPA will publish a Federal Register notice to take comment on adding regulatory text that will reflect EPA’s plain language reading of the statute
Wisconsin
Department of Natural Resources
Once In Always In Policy

## Slide 10: NSR reform
Lawmakers are looking to “ease the burden of EPA's new source review (NSR) air permitting program”
EPA responded with a December 7, 2017 memo deferring to industry's projections of likely emissions increases
  For facilities using projected actuals to show that a project does not require review under PSD
  EPA will not question a facility’s emission projections but will rely on post construction information to determine if projection was accurate
EPA expects this to be the 1st memo in a series of NSR reforms
Wisconsin
Department of Natural Resources

## Slide 11
EPA items on the horizon – Air monitoring citizen science
  Citizen science and low cost sensor technology
  EPA making an effort to support citizen science efforts
    sensor toolbox
    standards for sensor technology
Wisconsin
Department of Natural Resources

## Slide 12: 1-Hour NO2 NAAQS
Published in Wisconsin Administrative Code August 1, 2016
Criteria for permit approvability in Wisconsin Statute:
  Air program may not issue a permit unless if finds that the source cannot cause or exacerbate a violation of NAAQS
Wisconsin
Department of Natural Resources

## Slide 13: NO2 NAAQS in Permit Reviews
DNR will use dispersion modeling to evaluate NOx emissions for the 1-hour NO2 standards for the following application types:
Major construction permit reviews under Prevention of Significant Deterioration
  Modeling submitted with application as required in ch. NR 405
  Updated Ambient Ratio Method for conversion of NOx to NO2 to be used
  Updated 40 CFR Part 51 Appendix W to be used
Other permits at facilities with large fuel combustion units:
  National Emissions Inventory lists coal fired electric generating units and coal fired industrial boilers as the only significant stationary source contributors to NOx emissions
  Use PSD source category as a size threshold
Wisconsin
Department of Natural Resources

## Slide 14
DNR will use a weight of evidence approach to evaluate NOx emissions for the 1-hour NO2 standards for all other application types:
Weight of evidence of the impact industrial stationary sources have on ambient NO2 concentrations:
  Mobile sources, such as motor vehicles, are the primary source of NOx emissions (approximately 60%) that contribute to ambient 1-hour NO2 concentrations.
  Approximately 80 percent of the NOx emissions in Wisconsin come from sources that are not industrial stationary sources regulated by air pollution control permits.
  NOx emissions from industrial sources are decreasing over time due to more restrictive regulations and advances in technology.
Wisconsin
Department of Natural Resources
NO2 NAAQS in Permit Reviews

## Slide 15
Weight of evidence based on ambient air quality monitoring shows:
  All portions of the United States are in attainment with the 1-hour NO2 NAAQS
  Wisconsin, Minnesota, Iowa, and Illinois have NO2 concentrations of less than 75% of the 1-hour NAAQS, including the heavily populated Chicago metropolitan area and concentrations are steadily decreasing
  Ambient 1-hour NO2 concentrations show a consistent downward trend nationwide
  The regulation of industrial stationary sources of NOx, as well as advances in technology, is expected to further decrease ambient concentrations of NO2
Wisconsin
Department of Natural Resources
NO2 NAAQS in Permit Reviews

## Slide 16
Guidance on NO2 has been drafted including:
  Memo to permit writers: decision tree on when to use dispersion modeling and when to use weight of evidence
  Attachment to Wisconsin Modeling Guidelines containing references and technical information used to support weight of evidence
DNR posted guidance on September 29, 2017 and took public comment for 21 days
DNR is preparing the final guidance and response to comments
Final guidance is expected the first quarter of 2018
Wisconsin
Department of Natural Resources
NO2 NAAQS Implementation

## Slide 17: PM2.5 in Air Permits
New approach – treat PM2.5 like ozone
Make a finding using a “weight of evidence” approach, that standards are protected
  State-wide ambient monitoring data demonstrates that PM2.5 behaves like a “regional” pollutant
  Concentrations vary similarly across vast areas
  Analysis of ambient monitoring filters showing PM2.5 is mostly from secondary formation
  Direct emissions from stationary sources are MUCH lower than reported
Wisconsin
Department of Natural Resources
Notes: 17

## Slide 18
The only regulatory requirement for PM2.5 is the ambient air quality standards
  When is PM2.5 limit in a permit?
    Limits established to keep emissions below major modification thresholds, i.e. major NSR avoidance
    Limits established as BACT or LAER in major NSR
    Limits established at a level shown by a model to protect a standard
PM2.5 in Air Permits
Wisconsin
Department of Natural Resources
Notes: 18

## Slide 19
PM2.5 permitting: minor sources
PM2.5 limits will not appear in most minor source permits;
  Exceptions: Previously established limits
  PSD avoidance limits
Guidance provided on calculating PM2.5 emissions for permit writers and permit applicants.
Accurate emissions estimates of PM2.5 emissions are essential
  Fuel combustion\high temperature processes
Permitting Implications
Wisconsin
Department of Natural Resources

## Slide 20
PM2.5 permitting: major PSD sources
PM2.5 major modification avoidance limits will still be needed
PM2.5 will need to be in netting analyses
PM2.5 will be modeled as required in federal law
Even for PSD – accurate PM2.5 estimates are essential
  Fuel combustion and high temperature processes.
  Consider additional information or data if presented
Permitting Implications
Wisconsin
Department of Natural Resources

## Slide 21
Concentrations of PM2.5 have and continue to decrease due to appropriate regulation of PM2.5 precursors and sources
There are alternatives to dispersion modeling for determining whether a source’s emissions are protective of the NAAQS
Review recurring issues with EPA
Continually review and revisions to guidance on PM2.5 as needed
Summary and Next Steps
Wisconsin
Department of Natural Resources

## Slide 22: Collaborative Permit Process
Guidance on Collaborative Permit Process – Submitting a Redline Strikeout Version of an Existing Permit as Part of an Application
  Encourages facility submitting a permit application to include an edited version of an existing permit
  Shows permit applicants how to obtain editable versions of their permit documents
  Lists types of conditions that DNR cannot change
  Goal is to facilitate communication and increase overall efficiency of the permit process
Posted on February 22, 2018 and is available for 21 day comment through March 13, 2018 http://dnr.wi.gov/news/input/guidance.html
Wisconsin
Department of Natural Resources

## Slide 23
Waste & Materials Management
Program Update
Wisconsin
Department of Natural Resources

## Slide 24: WMM Program Topics
Rule Revisions
  NR 538 – Beneficial Reuse
  NR 600 series - Hazardous Waste
Legislation
  Exemption for iron & steel slag
  Pyrolysis & Gasification exemption
Wisconsin
Department of Natural Resources

## Slide 25: NR 538 Overview
NR 538.03(4) Specific high-volume industrial byproducts:
  Paper mill sludge
  Coal ash
  Flue gas desulfurization material (FGD)
  Foundry sand & slag
  Lime kiln dust
  Other non-hazardous solid waste with similar characteristics
Wisconsin
Department of Natural Resources

## Slide 26: Material Use
Specific uses of industrial byproduct allowed based on byproduct Category
  Category 1 = few restrictions on use
  Category 5 = most restrictions on use & placement
Wisconsin
Department of Natural Resources

## Slide 27: NR 538 Revision
TAC has met 7 times since spring 2016
Emphasis on keeping successful framework
Simplify process
Largely self-implementing
Expand number of approved uses
Improve material tracking
Wisconsin
Department of Natural Resources

## Slide 28: Hazardous Waste Regulation Revisions
Generator improvement rule
Definition of solid waste
e-Manifest
Wisconsin
Department of Natural Resources

## Slide 29
Legislation
  Exemption for iron and steel slag
    SB 792/AB941
    Status: Passage as amended; available for scheduling
  Pyrolysis and gasification exemption
    SB646/AB789
    Status: Passage as amended; available for scheduling
Wisconsin
Department of Natural Resources

## Slide 30
Questions?
Bart Sponseller
608-266-0014
Wisconsin
Department of Natural Resources